## Slide 1: Framework for Evaluating an IC’s Resiliency to Fabrication-Time Attacks (U)
Tim Trippel
Summer Research Intern – Final Presentation
August 29th, 2017
Notes: 1
1

## Slide 2: About Me
Purdue University
  BS in Computer Engineering
University of Michigan
  MSE in Computer Science Engineering
  PhD in Computer Science Engineering
    Focus in Hardware Security
Author of the “WALNUT” paper on controlling MEMS accelerometers with acoustics
Worked under Matthew Hicks & Kevin Bush

## Slide 3: Overview
Motivation
Problems
Preparation
Problem
Approach
Design
Results
Future Work

## Slide 4: Motivation
While the U.S. Gov. CAN create trustworthy IC designs, they cannot fabricate these designs with technology nodes < 90nm at trusted foundries.
Until 2016, hardware Trojans demonstrated in literature were easily detectable
  Trigger circuits too sophisticated  easily detectable via physical inspection/side channels
  Trigger circuits too simplistic  easily detectable via post-fab testing
Oakland 2016 best paper (A2: Analog Malicious Hardware) demonstrated how a sophisticated trigger circuit could be crafted out of analog components making it stealthy enough to avoid detection.
Design
(Trusted)
Fabrication
(Untrusted)

## Slide 5: Preparation
To study fabrication time attacks, must work with real IC design:
  OR1200 Open Source Processor SoC (same as A2 paper)
  Designed using 45nm ARM and IBM standard cell and I/O cell libraries
  Synthesized with Cadence Genus v16.23
  Placed and Routed with Cadence Innovus 17.1

## Slide 6: Problem
How do we deal with stealthy fabrication-time attacks?
  Detection
    Stochastic Backside Imaging – image only areas of chip where Trojan is likely to be
  Prevention
    Defensive Layout – make it difficult for an attacker to insert the Trojan to begin with
Need a framework to evaluate how difficult it is to insert Trojans at fabrication
  How do we identify security critical nets in a design?
  How do we evaluate how difficult it is to attach a rogue wire to a critical wire in a design?
security-critical wire
Trojan Circuit
rogue wire
IC

## Slide 7: Approach
RTL
Synthesis
Place & Route
Fabrication
ASIC Design Flow
Verilog
RTL
GDSII
Verilog
Netlist
Nemo
GDSII-Score
Framework Tool Flow
Security
“Score”
Verilog
Netlist
Signal
Prefix
GDSII
Critical
Nets

## Slide 8: Design
Assume: RTL designer has appended a specific prefix to “security critical” signal names in a design
Problem: Given this, how can we identify the “fan-in” to these security critical signals?
Solution: Nemo – a Verilog compiler back-end that outputs signal dependency graphs
Nemo Tool Flow
RTL
Synthesis
Place & Route
Fabrication
Identifying Security Critical Nets in a Design
ASIC Design Flow
Verilog
RTL
Verilog
Netlist
GDSII
Nemo
Critical Signal Dependency Graph
Verilog Netlist
(from synthesis)
Critical Sig Prefix
Nemo has been open-sourced: https://github.com/mit-ll/nemo

## Slide 9: Design
Nemo Example Usage
Nemo INPUT
(Synthesized Verilog Netlist)
Nemo
Nemo OUTPUT
(Graphviz .dot file)

## Slide 10: Design
Problem: Given a list of wires (output from nemo), how can we identify how difficult it is to attach a rogue wire to one?
Solution: GDSII-score – an automated framework for analyzing the layout of specific nets in a GDSII file
Evaluating the Difficulty of Attaching Rogue Wires to Critical Wires
GDSII-Score
Report
Critical Signal Dependency Graph
(Nemo Output)
GDSII
GDSII-Scroe Tool Flow
RTL
Synthesis
Place & Route
Fabrication
Verilog
RTL
Verilog
Netlist
GDSII
ASIC Design Flow
GDSII-Score will be open-sourced soon!

## Slide 11: Design
How does GDSII-Score Work?
GDSII-Score is an exstensible Python framework for analyzing security-critical path objects (wires) in a GDSII file.
class Layout():
LEF() – stores info about design rules
GDSII() – stores the GDSII data structures
CriticalNets() – Stores a list of security critical nets to examine (Nemo output)

## Slide 12: Design
Example GDSII-Score Use Case: Calculating Wire Blockage
Report:
Critical Net 1 is 65% Blocked

## Slide 13: Future Work
Oakland (IEEE Security and Privacy)
  Submit this work
Usenix Security
  Submit work on a “Defensive Layout” technique driven by this framework to make inserting Trojans at fabrication time very difficult
  Automate the generation of place & route tool scripts to maximize the “security” rating provided by the framework discussed today

## Slide 14: Acknowledements