## Slide 1: Framework for Evaluating an IC’s Resiliency to Fabrication-Time Attacks (U)
Tim Trippel
Summer Research Intern – Final Presentation
August 29th, 2017
Notes: 1
1

## Slide 2: About Me
Purdue University
  BS in Computer Engineering
University of Michigan
  MSE in Computer Science Engineering
  PhD in Computer Science Engineering
    Focus in Hardware Security
Author of the “WALNUT” paper on controlling MEMS accelerometers with acoustics
Worked under Matthew Hicks & Kevin Bush

## Slide 3: Overview
Motivation
Problem
Preparation
Approach
Design
Future Work

## Slide 4: Motivation
Hardware Supply-chain Security
Design Phase
Manufacture Phase
3rd Party IP
Untrustworthy Designers
Untrustworthy Tool Chain
Untrustworthy Foundry
Untrustworthy Source
Untrustworthy Delivery
Front End
Malicious design flaws
Back End
Malicious deviations from a trusted design

## Slide 5: Motivation
Hardware Supply-chain Security
Design Phase
Manufacture Phase
3rd Party IP
Untrustworthy Designers
Untrustworthy Tool Chain
Untrustworthy Foundry
Untrustworthy Source
Untrustworthy Delivery
Front End
Malicious design flaws
Back End
Malicious deviations from a trusted design
Untrusted
Trusted
Trusted

## Slide 6: Motivation
Assuming one CAN create trustworthy IC designs, how can you guarantee the fabrication of these designs at untrusted foundries?
Until 2016, hardware Trojans demonstrated in literature were easily detectable
  Trigger circuits too sophisticated  easily detectable via physical inspection/side channels
  Trigger circuits too simplistic  easily detectable via post-fab testing
Oakland 2016 best paper (A2: Analog Malicious Hardware) demonstrated how a sophisticated trigger circuit could be crafted out of analog components at fabrication time making it stealthy enough to avoid detection.
Design Phase
Manufacture Phase
Trusted
Untrusted

## Slide 7: Problem
How do we deal with stealthy fabrication-time attacks?
  Detection
    Stochastic Backside Imaging – image only areas of chip where Trojan is likely to be
  Prevention
    Defensive Layout – make it difficult for an attacker to insert the Trojan to begin with
Need a framework to evaluate how difficult it is to insert Trojans at fabrication time
  How do we identify security critical nets in a design? (Nemo)
  How do we evaluate how difficult it is to attach a rogue wire to a critical wire in a design? (GDSII-Score)
security-critical wire
Trojan Circuit
rogue wire
IC
Notes:     Obfuscation – make it difficult to reverse engineering to find security-critical wires

## Slide 8: Preparation
To study fabrication time attacks, must work with real IC design:
  OR1200 Open Source Processor SoC (same as A2 paper)
  Designed using 45nm ARM and IBM standard cell and I/O cell libraries
  Synthesized with Cadence Genus v16.23
  Placed and Routed with Cadence Innovus 17.1

## Slide 9: Approach
RTL
Synthesis
Place & Route
Fabrication
ASIC Design Flow
Verilog
RTL
GDSII
Verilog
Netlist
Nemo
GDSII-Score
Framework Tool Flow
Security
“Score”
GDSII
Critical
Nets
Verilog
Netlist
Signal
Prefix

## Slide 10: Design
Assume: RTL designer has appended a specific prefix to “security critical” signal names in a design
Problem: Given this, how can we identify the “fan-in” to these security critical signals?
Solution: Nemo – a Verilog compiler back-end that outputs signal dependency graphs
Nemo Tool Flow
RTL
Synthesis
Place & Route
Fabrication
Identifying Security Critical Nets in a Design
ASIC Design Flow
Verilog
RTL
Verilog
Netlist
GDSII
Nemo
Critical Signal Dependency Graph
Verilog Netlist
(from synthesis)
Critical Sig Prefix
Nemo has been open-sourced: https://github.com/mit-ll/nemo

## Slide 11: Design
Nemo Example Usage
Nemo INPUT
(Synthesized Verilog Netlist)
Nemo
Nemo OUTPUT
(Graphviz .dot file)

## Slide 12: Design
Problem: Given a list of wires (output from Nemo), how can we identify how difficult it is to attach a rogue wire to one?
Solution: GDSII-score – an automated framework for analyzing the layout of specific nets in a GDSII file
Evaluating the Difficulty of Attaching Rogue Wires to Critical Wires
GDSII-Score
Report
Critical Signal Dependency Graph
(Nemo Output)
GDSII
GDSII-Score Tool Flow
RTL
Synthesis
Place & Route
Fabrication
Verilog
RTL
Verilog
Netlist
GDSII
ASIC Design Flow
GDSII-Score will be open-sourced soon!

## Slide 13: Design
How does GDSII-Score Work?
GDSII-Score is an exstensible Python framework for analyzing security-critical path objects (wires) in a GDSII file.
class Layout():
LEF() – stores info about design rules
GDSII() – stores the GDSII data structures
CriticalNets() – Stores a list of security critical nets to examine (Nemo output)

## Slide 14: Design
Example GDSII-Score Metric: Calculating Wire Blockage
Report:
Critical Net 1 is 65% Blocked
Notes: As we approach smaller technology nodes there are more design rule constraints

## Slide 15: Design
Edit Distance
Open Space for Implant
Other GDSII-Score Metrics
Notes: Edit distance
Spider method

## Slide 16: Future Work
Nemo + GDSII-Score Framework
(Oakland 2018)
Stochastic Backside Imaging
(?)
Defensive Layout
(Usenix 2018)
Notes: Open questions:
How automate detection of security-critical signals
Advances in gds2-score metrics
Def. PnR – auto gen of critical paths
Imaging – generation of a distribution for image samplinge

## Slide 17: Future Work
Open Questions/Tasks:
How to automate selection of security-critical nets?
Developing more advanced GDSII-Score metrics.
Use the framework to produce a sampling distribution of high-valued locations on an IC to image.
Use the framework to auto-generate place-&-route scripts that add “guard-wires” to sensitive nets
Notes: Open questions:
How automate detection of security-critical signals
Advances in gds2-score metrics
Def. PnR – auto gen of critical paths
Imaging – generation of a distribution for image samplinge

## Slide 18: Acknowledgements
Mentors:
  Matt Hicks
  Kevin Bush
Group 81:
  Ted Lyszczarz
  Brian Tyrrell